## Slide 1: Introduction to VLSI Design
Session 1.1

## Slide 2: Overview of Digital Design Using Verilog
Evolution of Computer-Aided Digital Design
Emergence of HDLs
Typical Design Flow
Design Methodologies
Importance of HDLs
Popularity of Verilog HDL

## Slide 3: Evolution of Computer-Aided Digital Design
SSI: Small scale integration
  A few gates on a chip
MSI: Medium scale integration
  Hundreds of gates on a chip
LSI: Large scale integration
  Thousands of gates on a chip
  CAD: Computer-Aided Design
  Logic and circuit simulators
  Prototyping on bread board
  Layout by hand (on paper or a computer terminal)

## Slide 4: Evolution of Computer-Aided Digital Design (cont’d)
VLSI: Very Large Scale Integration
  Hundred thousands of gates
  Not feasible anymore:
    Bread boarding
    Manual layout design
  Simulator programs
  Automatic place-and-route
  Bottom-Up design
    Design small building blocks
    Combine them to develop bigger ones
  More and more emphasis on logic simulation

## Slide 5: Emergence of HDLs
The need to a standardized language for hardware description
  Verilog and VHDL (VHSIC HDL)
Simulators emerged
  Usage: functional verification
  Path to implementation: manual translation into gates
Logic synthesis technology
  Dramatic change in digital design
    Design at Register-Transfer Level (RTL) using an HDL

## Slide 6: VLSI IC Design Flow
Design specification
Behavioral description
RTL description
Functional verification and testing
Logic synthesis
Gate-level netlist
Logical verification and testing
Floor planning, automatic place & route
Physical layout
Layout verification
Implementation

## Slide 7
VLSI IC Design Flow

## Slide 8: VLSI IC Design Flow
Design specification
  In any design, specifications are written first.
  Specifications describe abstractly the functionality, interface, and overall architecture of the digital circuit to be designed.
  At this point, the architects do not need to think about how they will implement this circuit.
Behavioral description
  A behavioral description is then created to analyze the design in terms of functionality, performance, compliance to standards, and other high-level issues.
  Behavioral descriptions are often written with HDL

## Slide 9: VLSI IC Design Flow
RTL description
  The behavioral description is manually converted to an RTL description in an HDL.
  The designer has to describe the data flow that will implement the desired digital circuit.
  From this point onward, the design process is done with the assistance of EDA tools
  Functional verification and testing
  Simulation is the process of verifying the functional characteristics of models at any level of abstraction.
  We use simulators to simulate the Hardware models.
  To test if the RTL code meets the functional requirements of the specification, we must see if all the RTL blocks are functionally correct.
  To achieve this we need to write a testbench

## Slide 10
RTL Description
Functional Verification and Testing

## Slide 11: VLSI IC Design Flow
Logic Synthesis and Gate level Netlist
  The Logic synthesis tools convert the RTL description to a gate-level netlist.
  A gate-level netlist is a description of the circuit in terms of gates and connections between them.
  Logic synthesis tools ensure that the gate-level netlist meets timing, area, and power specifications.
  Logical verification and testing
After the synthesis there are a couple of things that are normally done before passing the netlist to backend (Place and Route)
Formal Verification : Check if the RTL to gate mapping is correct.
Scan insertion : Insert the scan chain in the case of ASIC.

## Slide 12: Synthesis Flow

## Slide 13: VLSI IC Design Flow
Floor planning, automatic place & route
  The gate level netlist from the synthesis tool is taken and imported into place and route tool in Verilog netlist format.
  All the gates and flip-flops are placed; clock tree synthesis and reset is routed.
  After this each block is routed.
  The P&R tool output is a GDS file, used by foundry for fabricating the ASIC
Physical layout
The gate-level netlist is input to an Automatic Place and Route tool, which creates a layout.
Layout verification and implementation
  The layout is verified and then fabricated on a chip

## Slide 14: Placement

## Slide 15: Final Layout

## Slide 16: Design Methodologies
There are two basic types of digital design methodologies: a top-down design methodology and a bottom-up design methodology
In a top-down design methodology, we define the top-level block and identify the sub-blocks necessary to build the top-level block. We further subdivide the sub-blocks until we come to leaf cells, which are the cells that cannot further be divided.
In a bottom-up design methodology, we first identify the building blocks that are available to us. We build bigger cells, using these building blocks. These cells are then used for higher-level blocks until we build the top-level block in the design

## Slide 17: 4-bit Ripple Carry Counter
Design Methodologies

## Slide 18: T-flipflop and the Hierarchy

## Slide 20: Importance of HDLs
Retargeting to a new fabrication technology
Functional verification earlier in the design cycle
Textual concise representation of the design
  Similar to computer programs
  Easier to understand

## Slide 21: Popularity of Verilog HDL
Verilog HDL
  General-purpose
  Easy to learn, easy to use
  Similar in syntax to C
  Allows different levels of abstraction and mixing them
  Supported by most popular logic synthesis tools
  Post-logic-synthesis simulation libraries by all fabrication vendors
  PLI to customize Verilog simulators to designers’ needs