## Slide 1: Maintenance Management PRERNA TOSHNIWAL

## Slide 2: Introduction to Maintenance
Management
 The dictionary defines maintenance as “the work of keeping something in proper condition, upkeep.” This would imply that maintenance should be taken to prevent a device or component from failing or to repair normal equipment degradation experienced with the operation of the devices to keep it in proper working order.
 Data obtained in many studies over the past decade indicates that most private and govt. facilities do not expend the necessary resources to maintain equipment in proper order. They wait for equipment failure to occur and then take whatever actions are necessary. Nothing lasts forever and all equipment has some predefined expectancy or operational life.

## Slide 3: Objectives of Maintenance
 Equipments should be kept in the best operating condition with economical cost.
 Minimize cost of maintenance
If a firm wants to be in business competitively, it has to take decision on whether to replace the equipment or to retain the old equipment.

## Slide 4: Types of Maintenance
 Breakdown (Reactive) Maintenance
It is basically the ‘run it till it breaks’ maintenance mode. No actions or efforts are taken to maintain the equipment as the designer originally intended to ensure design life is reached.
Advantages:
Involves low cost investment.
Less staff is required.
Disadvantages:
Increased cost due to unplanned downtime of equipment.
Increased labour cost, if overtime is needed.
Cost involved with repair or replacement of equipment.
Possible secondary equipment or process damage from equipment failure.

## Slide 5
 Preventive Maintenance
it can be defined as “Actions performed on a time or machine-run-based schedule that detect, preclude, or mitigate degradation of a component or system with the aim of sustaining or extending its useful life through controlling degradation to an acceptable level.”
 Advantages:
Cost effective in many capital intensive processes. (12% to 18%)
Flexibility allows for the adjustment of maintenance periodicity.
Increased component life cycle.
Energy savings.
Reduced equipment or process failure.
 Disadvantages;
Catastrophic failures still likely to occur.
Labour intensive.
Includes performance of unneeded maintenance.

## Slide 6
 Predictive Maintenance
It can be defined as “Measurements that detect the onset of a degradation mechanism, thereby allowing casual stressors to be eliminated or controlled prior to any significant deterioration in the component physical state.
Results indicate current and future functional capability.” It differs from preventive maintenance by basing maintenance need on the actual condition of the machine rather than on some preset schedule.
 Advantages:
Increased component operational life.
Allows for pre-emptive corrective actions.
Decrease in equipment or process downtime.
Decrease in costs for parts and labour.
Better product quality.
Energy savings.
Improved worker and environmental safety.
 Disadvantages:
Increased investment in diagnostic equipment.
Increased investment in staff training.

## Slide 7: Concept of Reliability in Maintenance
 Reliability is the probability of survival under a given operating environment. Ex; The consecutive failures of a refrigerator where continuous working is required is a measure of its reliability.
 Reliability or Failure rate= No. of units survived till the specific time
Total no. of units used

## Slide 8: Reliability Improvement
 Improved design of components.
 Simplification of product structure
 Usage of better production equipments
 Better quality standards
 Better testing standards
 Sufficient number of standby units
 Usage of preventive maintenance if necessary at appropriate time.

## Slide 9: Maintenance Planning Steps
 Knowledge base : t includes knowledge about equipment, job, available techniques, materials and facilities.
 Job investigation at site: It gives a clear perception of the total jobs.
 Identify and document the wok: Knowing the earlier two steps and knowing the needs of preventive, predictive and other maintenance jobs.
 Development of repair plan: Preparation of step by step procedures which would accomplish the work with the most economical use of time, manpower and material.
 Preparation tools and facilities list: Indicating the needs of special tools, tackles and facilities needed.
 Estimation of time required to do the job: with work measurement technique and critical path analysis.

## Slide 10: Maintenance Scheduling
 Scheduling is the function of coordinating all of the logistical issue around the issues regarding the execution phase of work. It deals with the questions- “Who would do the job?” and “When the job would be started and done?”
 Requirements for schedulers:
Manpower availability by trade, location, shift, crew arrangement and permissible overtime limit etc.
Man hour backlog on current or unfinished jobs.
Availability of the equipment or area where the work has to be done.
Availability of proper tools, tackles, spares, consumables, structural and other required materials.
Availability of external manpower and their capabilities.
Availability of special equipments, jigs, special lifting and handling
facilities and cranes etc.
Stating and completion date and time of jobs.
Past schedules and charts (updated).

## Slide 11: Maintenance Schedule Techniques
 The first step of all scheduling is to break the job into small measurable elements, called activities and to arrange them in logical sequences considering the preceding, concurrent and succeeding activities. The various techniques are:
Weekly general schedule is made to provide weeks worth of work for each employee in an area.
Daily schedule is developed to provide a day’s work for each
maintenance employee of the area.
Gantt charts are used to represent the timings of tasks required to complete a project.
Bar charts used for technical analysis which represents the
relative magnitude of the values.
PERT/CPM are used to find the time required for completion of the job and helps in the allocation of resources.

## Slide 12: Modern Maintenance Methods
 Reliability Centered Maintenance (RCM)
It recognises that all equipments in a facility is not of equal importance to either the process or safety. This indicates that equipment design and operation differs and that different equipment will have a higher probability to undergo failures from degradation. A facility does not have unlimited financial and personnel resources and that its use should be prioritized and optimised.
Advantages:
Lower costs by eliminating unnecessary maintenance.
Reduced probability of sudden equipment failures.
Increased component reliability.
Incorporates root cause analysis.
Disadvantages:
Can have significant startup cost, training, equipment etc.
Savings potential not readily seen by management.

## Slide 13
 Six sigma Maintenance
It is a process that focuses on reducing the variation in business production control i.e. a tighter control over its operational systems, increasing their cost effectiveness an encouraging productivity breakthrough. It is a term created by MOTOROLA to describe the goal and process used to achieve levels of quality improvement.
Steps:
This six sigma process is also known as DMAIC process. The steps are:
Define (Determining benchmarks, availability and reliability requirements,
mapping the flow process)
Measure (Development of failure measurement techniques, data collection , compilation and display)
Analysis (Checking and verifying the data and drawing conclusions, improvement opportunities, finding root causes)
Improve (creating model equipment and maintenance process, plan and schedule and implement those)
Control (Monitoring the improved programme, performances, make necessary adjustments for deviations)

## Slide 14
 Enterprise Asset Management (EAM)
It is an information management system that connects all departments and disciplines within a company making them an integrated unit. It is an organised and systematic tracking of an organisation’s physical assets(plant, machinery).It reduces paperwork, improves quality, quantity and timeliness of information.
 Lean Maintenance
This system recognises seven forms of waste in maintenance. They are over production, waiting, transportation, process waste, inventory, waste motion and defects. Efforts are made for the continuous improvement in process by eliminating wastes. It leads to maximise yield, productivity and profitability.

## Slide 15
 Computer Aided Maintenance
Such systems serve as effective decision support tool in the form of a well designed information system. Programmes are prepared to handle a large volume of data pertaining to men, money and equipment and can be used as and when required for effective performance of maintenance tasks.
Computer based maintenance systems:
Job card system – Job card shows the plant code, equipment code, job code, the nature of the jobs, the start time and finishing time, man-hour spent and etc. The use of computer facilitates the issue of job cards, recording job history and control of manpower.
Spare part life monitoring system – This is the recording of a description, anticipated life and date of installation of an equipment. When a spare part is replaced during breakdown failures or scheduled maintenance, the updating of information is done.
Spare parts tracking system- A file is created that contains the material code, spare part identification number, the assembly number and the place of part used. This helps in knowing the current position about a particular spare part and facilitates timely requirements.

## Slide 16
 Total Productive Maintenance (TPM)
The goal of TPM is to increase production while, at the same time, increasing employee morale and job satisfaction. The goal is to hold emergency and unscheduled maintenance to a minimum. It can be considered as a medical science of machines.
Objectives of TPM:
Avoid wastage in a quickly changing environment.
Producing goods without reducing product quality.
Reduce cost.
Produce a low batch quantity at the earliest possible time.
Goods send to the customers must be non-defective.

## Slide 17
 Similarities between TPM & TQM (Total quality Management)
1) Total commitment to the program by upper level management is
required in both programmes.
2) Employees must be empowered to initiate corrective action.
3) A long-range outlook must be accepted as TPM may take a year or
more to implement and is an on-going process.
 Difference between TPM & TQM
Category | TQM | TPM
Object | Quality (output and effects) | Equipment (Input and cause)
Mains of attaining | Systemize the management | Employees participation
Goal | It is software oriented | Hardware oriented
Target | Quality for PPM (Power production management0 | Elimination of losses and wastes

## Slide 18: Pillars of TPM
5S
Autonomous Maintenance Kaizen
Planned Maintenance Quality Maintenance Training
Office TPM
Safety, Health & Environment

## Slide 19: Pillar 1- 5S
 Problems cannot be clearly seen when the work place is unorganised.
Cleaning and organising helps the team to uncover problems. This is the
first step of improvement.
 SEIRI – Sort Out (Sorting and organising the items as critical, important, frequently used items, useless, or items that are not in need )
 SEITON – Systematise (Each item has a place and only one place. Items should be placed back after use)
 SEISO – Sweep (Cleaning the workplace free of burrs, grease, oil, waste, scrap etc. No loosely hanging wires or oil leakage from machines)
 SEIKETSU – Standardise (Employees have to discuss together and decide on standards for keeping the workplace/ machines/ pathways neat and clean)
 SHITSUKE – Self-discipline (This self-discipline rule includes wearing badges, following work procedures, punctuality, dedication to the organisation)

## Slide 20: Pillar 2 – Jishu Hozen (Autonomous
Maintenance)
 This pillar is geared towards developing operators to be able to take care of small maintenance tasks, thus freeing up the skilled maintenance people to spend time on more value added activity and technical repairs.
 Steps in Jishu Hozen:
Train the employees
Initial cleanup of machines
Counter measures
Tentative standard
General inspection
Autonomous inspection
Standardization
Autonomous management

## Slide 21: Pillar 3 - Kaizen
 ‘Kai’ means change, and ‘Zen’ means good (for the better). Kaizen is for small improvements, but carried out on a continual basis and involve all people in the organisation. It requires little or no investments.
 Kaizen Policy:
Practice concepts of zero losses in every sphere of activity.
Relentless pursuit to achieve cost reduction targets in all resources.
Relentless pursuit to improve overall plant equipment effectiveness.
Extensive use of PM analysis as a tool for eliminating losses.
Focus of easy handling of operators.

## Slide 22:  Tools used in Kaizen:
PM analysis
Why-Why analysis
Summary of losses
Kaizen register
Kaizen summary sheet
 16 Major losses in an organisation:
Breakdown loss
Adjustment loss
Cutting blade loss
Start up loss
Idling loss
Speed loss
Rework loss
Management loss
9) Scheduled downtime loss
10) Operating motion loss
11) Line organisation loss
Logistic loss
Measurement loss
Energy loss
Die, jig and tool breakage loss
Yield loss

## Slide 23: Pillar 4 – Planned Maintenance
 It is aimed to have trouble free machines and equipments producing defect free products for total customer satisfaction.
 Policy:
Achieve and sustain availability of machines
Optimum maintenance cost
Reduces spares inventory
Improve reliability and maintainability of machines.
Steps:
Equipment evaluation and recoding present status.
Restore deterioration and improve weakness
Building up information management system.
Prepare time-based information system, select equipment.
Prepare predictive maintenance system by introducing equipment diagnostic techniques.
Evaluation of planned maintenance.

## Slide 24: Pillar 5 – Quality Maintenance
 It is aimed towards customer delight through highest quality by defect free manufacturing. Transition is from reactive to proactive (Quality control to quality assurance).
 Policy:
Defect free conditions and control of equipments.
QM activities to support quality assurance.
Focus of prevention of defects at source.
Focus on fool proof system.
In-line detection and segregation of defects.
 Data Requirements
Customer end line rejections
Field complaints

## Slide 25: Pillar 6 - Training
 It is aimed to have multi-skilled revitalized employees whose morale is high and who is eager to come to work and perform functions independently and effectively. Education is given to operators to upgrade their skill.
 Policy:
Focus on improvement of knowledge, skills and techniques.
Creating a training environment for self learning based on felt needs.
Training curriculum/tools/assessment etc.
Training to remove employee fatigue and make work enjoyable.
 Steps:
Preparation of training calendar.
Evaluation of activities and study of future approach.
Setting training policies and establish training systems.
Up gradation of operation and maintenance skills.

## Slide 26: Pillar 7 – Office TPM
 Office TPM should be started after activating four other pillars of JH, KK, QM,PM. This includes analyzing processes and procedures towards increased office automation.
12 major losses of Office TPM | Benefits of Office TPM
1) Processing loss | 1) Involvement of all people
2)Cost and Inventory loss | 2) Better utilised work area
3) Communication loss | 3) Reduced repetitive work
4)Idle loss | 4) Reduced inventory levels
5)Set-up loss | 5) Reduced administrative cost
6) Accuracy loss | 6) Less inventory carrying cost
7) Office equipment breakdown | 7) Reduction in number of files
8) Communication channels loss | 8) Reduction of overhead costs
9) Time loss on information | 9) Productivity of people
10) Non availability of stock status | 10) Clean work environment
11) Customer complaints | 11) Less customer complaints
12) Expenses on emergency | 12) Reduced manpower

## Slide 27: Pillar 8 – Safety, Health & Environment
 Target:
Zero accident
Zero health damage
Zero fires
A safe workplace and a surrounding area that is not damaged by our process or procedures. This pillar will play an active role in each of the other pillars on a regular basis. Utmost importance to safety is given to the plant.