## Slide 1: STUDY OF SOURCES OF FARM POWER
Class-1

## Slide 2: INTRODUCTION
A farm power for various agricultural operations can be broadly classified as:
(1) Tractive work such as seed bed preparation, cultivation, harvesting and transportation, and
(2) Stationary work like silage cutting, feed grinding, threshing, winnowing and lifting of irrigation water.
These operations are done by different sources of power, namely human, animal, oil engine, tractor, power tiller, electricity and renewable energy (biogas, solar and wind).

## Slide 3
Farm Power in India
Indian is the highest producer of tractor in the world with annual production of 548397 tractors(2010-11)
Total population of tractor is about 4.0 million
Annual sale of power tillers in India is about 35000
Total population of power tiller in India is about 3 lakh.
Diesel engine population 76 lakh
Electric motor population 12 million.
Out of 342 m workforce 224 m(66%) are agril. Workers.
Draft animals are 74 million
Average land holding is 1.6 ha (India) and 1.25 ha (Odisha).
67% land area is rainfed

## Slide 4: Sources of Farm Power
Human Power
Animal Power
Mechanical Power
Tractors
Power tillers
Self Propelled combines
Oil Engines
Diesel Engine
Petrol/Kerosene engine
Electric Power
Renewable energy
Notes: Food is largest consumption category in India.
The simplest reason for India’s consumption being so big is ….. POPULATION.

## Slide 5
Human Power
224 million agricultural workers out of total 342 million workers
Contribution of power is only 5.09 % of the total power
Most important source of power for operating small implements and tools.
On an average a man can develop 0.1 hp
Advantages
Easily available
Used for all types of work
Disadvantages
Costliest source of power
Very low efficiency
Requires full maintenance when not in use
Affected by weather condition and season.

## Slide 6
Animal Power
71million animals in India
Contribution of draft animals is 6.37 per cent
Employed for mostly tractive work but can be employed for all types of work.
On an average a pair of bullock can develop 1 hp
Other animals like buffalo, camel, horse, donkey, mule and elephant are also used for farm work.
Advantages
Easily available
Used for all types of work
Low initial investment
Supplies manures to field and fuel to farmers
Lives on farm produce
Disadvantages
Not very efficient
Season and weather affect efficiency
High over load capacity
Can not work at a stretch
Requires full maintenance when not in use

## Slide 7
Mechanical Power
Tractors, Power Tillers, Oil Engines and P Engines are the main source of mechanical power
Population of tractor, power tiller and Diesel engine in India is about 40, 3 and 76 lakhs, respectively.
Contribution of tractor and power tiller is about 51.08 %, stationery engine contributes 37.46 per cent. (Total contribution of non-animate power is 88.54 per cent)
Advantages
Efficiency high
Not affected by weather
Requires less space
Cheaper form of power
Disadvantages
Initial investment is high.
Does not require full maintenance when not in use

## Slide 8: TRACTOR
Tractors are available in following classes, depending upon Hp.
20-30 hp(About 25% of total production in India)
31-40 hp(About 60% of total production in India)
41 and above (About 15% of total production in India)
Tractor production started in India in 1961
The first tractor manufacturer , M/S Eicher Good earth at Faridabad.
Average command area of a tractor (26.1kw)/35hp is about 15 hectares.

## Slide 9: POWER TILLER
Power range of power tiller 5.97 to 8.95kw(8 to 12 hp)
Average command area of power tiller is 5 hectares.
One pair of bullock have the command area of 1 hector.

## Slide 10: OIL ENGINE
The oil engine is a highly efficient device for converting fuel into useful work.
The efficiency of diesel engine varies between 32 and 38 per cent, whereas that of the carburetor engine is in the range of 25 and 32 per cent.
In recent years, diesel engines and tractors have gained considerable popularity in agricultural operations.
Small pumping sets within 3 to 10 hp range are very much in demand.
Likewise, oil engines of low to medium speed developing about 14 to 20 hp are successfully used for flourmills, oil ghanis, cotton gins, etc.
Diesel engines of the larger size are used on tractors.

## Slide 11
Electrical Power
Electrical power mostly used in farm in the form of electrical motors.
Used for lifting water, running stationery machines, diary, processing, poultry farms.
About 12 million electric motors in use in Indian agriculture.
Advantages
Clean, quiet and cheap source of power
High efficiency
Can work at a stretch
Maintenance and operating cost is very low.
Not affected by season.
Disadvantages
Initial invetsment is high
Requires good technical knowledge

## Slide 12
Renewable Energy
Mainly bio-energy, wing energy and solar energy are suitable for Indian agriculture.
Used for water lifting, drying, lighting, water heating, food processing, domestic use, engine operation and electricity generation.
Advantages
No atmospheric pollution
Inexhaustible in nature
Disadvantages
Seasonal in nature
Location specific.
Low efficiency