## Slide 1: Intake and Exhaust System

## Slide 2
The intake and exhaust system deals with the inflow of fresh air and the outflow of used gases in the engine.

## Slide 3: AIR INTAKE SYSTEM
This system allows fresh air to enter the engine. Its main parts are:
(i) air cleaner,
(ii) supercharger (auxiliary unit),
(iii) intake manifold,
(iv) intake port and
(v) intake valve.

## Slide 4: AIR CLEANER
The operating efficiency, good performance and durability of an engine depend mainly upon its cleaner.
It is a device, which cleans and filters the air before entering the combustion chamber of an engine.
An IC engine uses large quantities of air for combustion, the ratio being 14-15 lb of air for every lb of fuel bursts.
The volume of the air used is about 10,000 gal/gal of fuel. Unfiltered air may contain millions of particles of abrasive dust and other matter, which could cause rapid wear.

## Slide 5
There are many types of air cleaners but the types commonly used in tractors are:
(i) Oil wetted mesh type,
(ii) Dry air type and
(iii) Wet type or oil bath air cleaners.

## Slide 6: OIL WETTED MESH AIR CLEANER
It consists of a copper mesh or nylon wire wetted with oil to catch the dust particles from the air which are made to pass through it.
This type, however, gets clogged with dust quickly, thus, seriously affecting the air flow through it and rendering it inefficient in removing the fine particles of dust from the air.

## Slide 7: DRY AIR CLEANER
This type of air cleaners contains three main parts, viz. pre-cleaner, main housing and cleaning element.
These are sealed into one unit.
The main housing contains the cleaning element, usually of multi-wire netting, but some are made of nylon hair or paper.
The air from the atmosphere enters from the pre-cleaner, passes through the cleaning element and goes to the inlet manifold.
The paper filter element is cleaned after 50-100 hours of service.
Dry air cleaners are mounted
(i) vertically in front of the tractor radiator and
(ii) horizontally on the overhead engine.

## Slide 8
The following are the advantages of the dry air cleaner:
1. Easy to service.
2. Good performance in gradient and in rough fields.
3. More efficient at high speeds.
4. Straw and chaff cause less restriction to air passage.
Its main disadvantages are:
It is costlier to maintain than an oil bath because the filter elements require replacements very often.
Sometimes, dust particles enter the cylinder