## Slide 1: INDUSTRIAL STERILIZATION ON LARGE SCALE
Deepankar ratha
Assistant professor,
CUTM,Rayagada

## Slide 2: STERILIZATION
Sterilization can be defined as the process through which all forms of life are destroyed, removed or permanently inactivated.
Sterilization is essential concept at large scale as well as small scale for the preparation of sterile pharmaceutical products.

## Slide 3
It’s aim is to provide a product that is safe and eliminates the possibility of contamination.

## Slide 4: WHY
To reduce amount of
contaminant’s
present in environment, on surface of container’s, closure’s as well as equipment’s and to achieve better sterile condition.

## Slide 5: SOURCE’S
Raw materials
Equipment & instrument’s
Manufacturing process
Container & closure system
Manufacturing environment
Worker’s

## Slide 6: STERILIZATION PROCESSES
The sterilization is done by
  Physical method
  Chemical method

## Slide 7: Physical Method
Moist heat
  saturated steam autoclave
  superheated water autoclave
  air over steam autoclave
Dry heat
  continuous tunnel sterilizer
  hot air oven
  Red heat
  Flaming

## Slide 8
Radiation
  Non-ionizing radiations
    Ultraviolet (UV) light
  Ionizing radiations(cold sterilization)
    X-rays
    Gamma rays
    Cathode rays

## Slide 9
Filtration
Depth filter
  sintered glass filter
Screen filter
  particulate filter
  microbial filter

## Slide 10: Chemical Method
Chemical sterilization
  Gaseous sterilization
    Ethylene oxide
    Formaldehyde
  By using disinfectant or antimicrobial agent

## Slide 11: PROCESS SELECTION
Process selection is most important and sensitive point for preparation of product.
Those product intended to be sterile should be terminally sterilized in their final container as clearly stated in EUROPIAN PARMACOPOEIA.
Where it is not possible to carry out terminal sterilization, choose the alternative method.

## Slide 12
describe | in | p’copoeia | may be
developed |  | to provide | sterility
It is recognised that new terminal sterilization process other than those
assurance level equivalent to present official method, & such process when properly validated may offer alternative approaches.

## Slide 13
The use of an inappropriate heat labile packaging material can not in itself be the sole reason for adoption of aseptic processing, rather manufacturers should choose the best sterilization
method achievable
a given
for
formulation & select the packaging
material accordingly.

## Slide 14
The choice of packaging material for given product has to take into account factors other than the method of sterilization.
In such cases these other factor need to be clearly documented, explained & scientifically justified.

## Slide 15: PROCESS FOR AQUEOUS PREPARATIONS
If the product is aqueous
Can product be sterilize by moist heat at 121°C for 15min
Use autoclaving at 121°C for 15min
Can the product be
sterilize by moist heat
withF0 ≥8 min
Use moist heat with F0 ≥8 min
Can the formulation
be filtered through a microbial retentive filter

## Slide 16: Use pre sterilized individual component & aseptic compounding & filling
Use combination of aseptic filtration & aseptic processing

## Slide 17: If the product is non-aqueous, semi solid or dry powder
Can the product be sterilized by dry heat at 160°C for 120min
Use sterilization at 160°C for 120 min
Can the product be
sterilized by dry heat with an alternative combination of time & temp° so the standard cycle achieving an SAL of
≤10-6

## Slide 18: Use dry heat with an alternative combination of time & temp° so the standard cycle achieving an SAL of ≤10-6
Can the product be sterilized by a method different from dry heat
e.g. ionization
Can the sterilized by validated lower irradiation dose
Use a method different from dry heat e.g. ionization

## Slide 19: Use the sterilized by validated lower irradiation dose
Can the formulation be filtered trough a microbial retentive filter
Use pre-sterilized individual components & aseptic compounding & filling
Use filtration & aseptic
technique

## Slide 20: SPECIFICATIONS
MOIST HEAT STERILIZATION
  Micro organisms destroyed by cellular protein coagulation
  The objects to be sterilized are exposed to saturated steam under 1 atmosphere pressure at a minimum temperature of 121°C for 15 min.
  An autoclave is commonly used for moist heat sterilization.
  Because it does not require as high a tempº, moist heat sterilization cause less product and equipment damage compared to dry heat sterilization.

## Slide 21: AUTOCLAVE
team at |  | 
Temp°C 115-118 121-124 126-129 | lb/sq.inch 10 15 20 | Time(min) 30 15 10
Is a device to sterilize equipment and supplies by subjecting them to high pressure saturated s
135-138 30 3
TYPES
Portable autoclave (Bench autoclave)
Stationary autoclave (Large sterilizer)

## Slide 23
Main Features
  Lid(door) fitted with clamps and asbestos jacket , stationary autoclave may be double doors at both ends one for loading and one for unloading.
  Pressure gauge
  Thermocouple for measurement of tempº.
  Air vent to remove air before sterilization.
  Safety valve to permit escape of excess steam to prevent explosion .
  Modern autoclaves are recording (record pressure, temp during the whole process ) supplied with timer and are automatically controlled .

## Slide 24
DRY HEAT STERILIZATION
  Is appropriate for materials that cannot withstand moist –heat sterilization (e.g., oily materials and powders)
  Objects are subjected to a temperature of at least 160º for 120 minutes( if higher temperatures can be used , less exposure time is required)

## Slide 25: HOT AIR OVEN
Is a device to sterilize subject and supplies by subjecting them to direct heat at
Temp°C | Time(min)
170 | 60
160 | 120
150 | 150
140 | 180
Is appropriate for the materials that can not withstand steam sterilization (e.g. oily materials & powders)
If higher temperature can be used, less exposure time is required.

## Slide 27
Main Features
  Door fitted with the clamps and asbestos jacket has the single door
  Regulator for temperature control
  Fan attached inside for air circulation
  Perforated shelf for keeping subject inside

## Slide 28
RADIATIONS
  Energy transmitted through space in variety of forms is generally called radiation
  This method is also called as cold sterilization because it produce relatively little heat
  Thus, it is possible to sterilize heat sensitive materials such techniques are being in food industries mainly

## Slide 29
Non ionizing radiations (UV)
  UV in region of 2537 A° has been shown to posses the greatest activity in destroying MO
  Commonly employed in reduction of air- borne contamination in the maintenance of aseptic areas & rooms
  Source of artificial UV radiation s is UV lamps (generally called sterilizing lamp or germicidal lamp)
  UV light is absorbed by the nucleic acid of the cell where it does the greatest damage

## Slide 31
Ionizing radiations (cold sterilization)
  X-rays, gamma rays & cathode rays are lethal to DNA & other vital cell constituents
  They have high penetration power & considerable energy
  The factors that effect the lethal activity of ionizing radiations are oxygen effect, protective compounds, sensitizing agents, pH of cultures, freezing, moisture & recovery conditions

## Slide 32
Filtration
  This is a non-thermal method of sterilization used widely in the p’ceutical industry where heat labile solutions are to be sterilized
  This is useful for large volume solutions, eye drops, antibiotic solutions, sera & carbohydrate solutions
This also useful
bacteriophages & bacterial toxins
for separation of
from
bacteria for the isolation of MO which are scanty in fluids

## Slide 33
3 main stages involved in filtration
of the solution through a sterilized bacteria-proof filter
1. Passage previously unite
Aseptic transference of filtrate to sterile containers then sealed aseptically
Testing of sample for sterility

## Slide 34
Gaseous sterilization
  The destruction of all living MO with chemical in gaseous or vapours state
  When material is affected by the dry or moist heat then the gaseous sterilization is used
  All these gases are toxic to human being above certain conc. and may exhibit other undesirable side effect
  Ethylene oxide is most widely used gaseous sterilization agent in pharmaceutical industry
  In addition to these, various glycols, methyl bromide and alcohol have been used for room sterilization

## Slide 35
conc.(mg/lit) | exposure
e(hrs.) | 
44 | 24
88 | 10
442 | 4
Ethylene oxide
  It is colorless liq. with BP 10.8°C
  Highly inflammable and may be explosive when mixed with air in conc. Greater than 3%. Its mixture with CO2 in certain proportion makes it inflammable
  Conc. & time relationship commonly for sterilization is as below
ti
884
2

## Slide 36
Disinfectant or antimicrobial agents
  Chemical agents most commonly used as disinfectant ant antiseptic e.g. phenols, alcohols, halogens, dyes, aldehyde etc.

## Slide 37: DEVELOPMENT & VALIDATION OF PROCESS & EQUIPMENT
Process validation:
It is analysis of data gathered throughout the design & manufacturing of product in order to confirm that the process can reliably output products of determined standard.
Regulatory authorities like EMA & FDA have published guidelines relating to process validation

## Slide 38
The purpose of validation is to ensure varied inputs lead to consistent & high quality outputs
Process validation is an ongoing process that must be frequently adapted as manufacturing feedback is gathered
End to end validation & production is essential in determining product quality because quality can not always be determined by finished product inspection

## Slide 39
Process validation can be broken in to 3 steps
  Process design
  Process qualification
  Continued process verification
Process design:
In this data from the development phase are gathered & analyzed to define the commercial manufacturing process. The data used to establish benchmark for quality & production control

## Slide 40
Process qualification:
In this stage the process design assessed to conclude if the process is able to meet determine manufacturing target. All the process & manufacturing equipment is proofed to confirm quality & output capabilities
Continued process validation:
It is the ongoing monitoring of all aspects of production cycle. It aims to ensure that all levels production are controlled & regulated

## Slide 41: EQUIPMENT VALIDATION/ QUALIFICATION
Equipment validation is divided into
  Design qualification
  Installation qualification
  Operational qualification
  Performance qualification

## Slide 42
DQ:
It define the functional & operational specification of the instrument & details for the continues design in selection of supplier
IQ:
Demonstrates that the process or equipment meets all specifications, is installed correctly, and all required components and documentation needed for continued operation are installed and in place.

## Slide 43
OQ:
Demonstrates that all facets of the
or equipment are operating
process correctly.
PQ:
It is the process of demonstrating
that an instrument
consistently performed according to specification
appropriate for it’s routine work