## Slide 1
Protective Devices used in Microgrid System: Lightning Arrestor

## Slide 2: Lightning Arrestor
A device used on power systems of above 1000V to protect other equipment from Lightning & Switching surges.
Other devices similar to Lightning Arrestors are :
SPD (Surge Protective Device) This is also a surge diverter, but generally for voltages well below 1000 volts.
TVSS (Transient Voltage Surge Suppressor) Again this is also a surge diverter, but generally for voltages well below 1000 volts.

## Slide 3: Function Lightning Arrestor
It does not absorb the Lightning
It does not stop the Lightning
It does divert the Lightning to ground
It does clamp (limit) the Voltage produced by the Lightning
It Only protects equipment electrically in parallel with it.

## Slide 4: Types of Lightning Arresters
The lightning arrestor is mainly classified into twelve types. These types are :-
  Road Gap Arrester
  Sphere Gap Arrester
  Horn Gap Arrester
  Multiple-Gap Arrester
  Impulse Protective Gap
  Electrolytic Arrester
  Expulsion Type Lightning Arrester
  Valve Type Lightning Arresters
  Thyrite Lightning Arrester
  Auto valve Arrester
  Oxide Film Arrester
  Metal Oxide Lightning Arresters