## Slide 1: Session-6
Factors to be considered while designing a livestock farm

## Slide 2
Factors to be considered while designing a livestock farm
Different types of enterprises such as dairy, piggery, sheep and goat units need different building design. So the design should be prepared to meet the need of a particular enterprise.
Each enterprise may adapt different systems of production and management. The design may be influenced by enterprise also. The following factors may be considered while designing a dairy farm-

## Slide 3
Designing for unit
It is desirable to design the accommodation for a workable unit.
It will give opportunity to study the need of smaller group with regard to floor space, feeding space required for different kinds of animals.

## Slide 4
2. Structural form
Shape and design of building should meet the needs of all classes of livestock.
Uniformity in the appearance should be maintained. We have to decide the number of animals to be housed in thebuilding and number of buildings to be constructed.

## Slide 5
3. Designing for flexibility
Animal building has to be designed to meet the requirement of changing enterprises.
This will increase the utility of buildings. Spacious building without pillars can be easily being adopted for differententerprises with little modifications in the building.
For example large intensive dairy buildings can be used for rearing pig or sheep and goat with little modification.

## Slide 6
4. Shape of the roof
It is designed to suit the local climatic conditions. Gable with roof ventilator is necessary for hot condition.
Monitor roof is suitable for building with smaller width.

## Slide 7
5. Standard width of buildings
Single row cow shed should have length of 3. 80 to 4.25 metres and
Double row cow shed should have 7. 90 to 8.70 metres length.

## Slide 8
6. Standard height of the building
The standard height of the building may differ according to the roofing material and agro climatic condition.
7. Length of building
The standard length of building may be of any. It may vary depends upon the number of animals housed.
Length can be determined based on the total stock to be housed within the building.
Example: In case of dairy 15-20 animals in single row system and 20-50 animals in double row system and above 50animals a separate shed should be provided.

## Slide 9: Thank You