## Slide 1: ARSON

## Slide 2
The term “arson” is commonly used today to describe a crime that involves the intentional burning of property. “the act of burning.” The common law definition of arson was the willful and malicious burning of a dwelling; over the years. Most of today’s arson laws involve the intentional burning of property, not only dwellings.

## Slide 3
The actions of a fire department at the scene can be separated into three distinct phases: (1) suppression, (2) overhaul, and (3) investigation. During the fire suppression phase, the first goal is to save lives; the second goal is the suppression of fire and the protection of property.

## Slide 4
The final phase of fire scene activities involves the investigation of the fire with the intent of determining its origin and cause. Although this is identified as the final phase, the investigation of the fire scene can actually begin during the suppression or overhaul phase.

## Slide 5
The commencement of the investigation depends largely on the time of arrival of the fire investigator or the abilities and responsibilities of the fire suppression personnel. Fire investigators will attempt to determine whether the fire was accidental or intentionally set (incendiary). Upon completion of the fire scene investigation, the property is typically released to the property owner or insurance company

## Slide 6
As previously discussed, fire is enormously costly to society. Fire departments across the country are required to investigate fires to determine the origin and cause. A fire occurs when a fuel comes together with oxygen and a heat source. It is the role of the fire investigator to determine how and why these

## Slide 7
factors came together and to answer the question: “Was this an accident or an intentional act?” It is not only the role of the fire department to suppress the fire but also to identify the cause of the fire.

## Slide 8
The two primary reasons that fires are investigated are to determine what caused the fire and to identify and collect any evidence related to that cause.
The purpose in determining the cause of the fire is to prevent the situation from occurring again. This is accomplished by identifying hazardous conditions or practices, product failures, or other fire causes. Once the cause is known, officials can educate the public or seek code changes in an effort to limit similar types of fires.

## Slide 9
Products suspected of causing fires can be examined more closely and modifications can be made or recalls issued in an effort to take corrective action. The second reason to investigate fires is to obtain evidence necessary to hold accountable the person or entity responsible for the cause — particularly in the case of an intentionally set fire. If the fire is determined to have been set, investigators will search for clues in the ashes in an effort to solve the crime

## Slide 10
The safety of the fire investigators and other investigative personnel working in and around fire scenes should be of utmost concern. Fires can cause a great deal of destruction and, as a result, dramatically impact the stability of a structure. Personnel involved in a fire investigation typically must enter the structure in an attempt to determine the origin and cause of the fire, document the scene, and collect appropriate evidence

## Slide 11
It is paramount that these activities are conducted in a safe manner and that personnel are provided with the proper safety equipment, Working in and around fire scenes can be inherently dangerous, and the proper safety measures should be followed for every investigation

## Slide 12
Prior to entering the fire scene, the investigator should make an assessment of the exterior of the structure to evaluate potential hazards. Close attention should be paid to any nonsupported or partially supported building components (walls, floors, roofs, stairs) that may have the potential for collapse .The location and status of all utilities (gas, water, electricity) should be determined as well as the presence of any hazardous materials .

## Slide 13
hazardous situations that they have found during their fire suppression efforts. In addition, the fire department may be able to monitor the environmental conditions inside the structure, including the levels of oxygen, carbon monoxide, or other contaminants, with the use of an air monitor.

## Slide 14
One of the greatest safety hazards at a fire scene can be airborne contaminants. With the use of synthetic materials in household and commercial products, fire investigators are frequently exposed to respiratory hazards while conducting investigations. In a typical structure fire, products containing plastics, foams, insulation, paints, and fibers are nearly always present. When these materials are involved in fire, they can liberate gases and vapors as well as aerosols, fibers, and particles.

## Slide 15
Combustion products typically found at a fire scene include carbon monoxide,hydrogen cyanide, oxides of nitrogen, and aldehydes (formaldehyde).
Exposure to these contaminants can produce both acute (immediate) and chronic toxic effects.
2 Protection from respiratory hazards in the form of gas, vapor, or particulate material must be considered. Inexpensive air-purifying respirators can be worn in a fire scene with little discomfort and do not hamper
the investigator’s ability to examine the scene

## Slide 16
Other health and safety issues at the fire scene include electrical activity, pooled water, confined spaces, biological hazards, and low lighting conditions.
One of the primary safety considerations at the fire scene is the public utility service to a structure. Fire departments will typically secure the electrical service to a residential or light commercial structure by removing the electric meter.
Gas service is easily controlled by the closure of a valve at the gas meter. Although the fire department may have terminated electrical activity to a structure, any electrical device or wiring should be treated as if energized until it is fully evaluated by the fire investigator. On occasion, a building may have more than one electrical service that is not apparent to the fire department or utility company and therefore not deactivated.

## Slide 17
Building occupants may have installed nonapproved wiring or may have illegally run electrical service from nearby structures; where present, these sources need to be deactivated. It is recommended that an alternating current (AC) voltage detector or similar device is utilized to detect the presence of any voltage prior to handling electrical wiring. These detectors are inexpensive and provide a great deal of safety when working in and around a fire scene.

## Slide 18
Pooled water is also a concern, especially when conducting an investigation in a basement or on a concrete slab. What looks like a shallow pool of water may actually be a deep sump pit or other opening in the floor. Water in the structure can also contain bio-hazards (sewage, infectious waste),particularly in abandoned buildings where homeless individuals may have loitered or others have utilized the structure for criminal activities.

## Slide 19
The National Fire Protection Association’s Guide to Fire and Explosion Investigations (NFPA 921) defines the scientific method as
The systematic pursuit of knowledge involving the recognition and formulation of a problem, the collection of data through observation and experiment, and the formulation of testing and
hypothesis.
NFPA 921 further explains how each step of the scientific method is applied to fire investigations.

## Slide 20: Fire Scene Examination
A safe and successful fire scene examination is conducted in a reasoned and systematic manner following established procedures. The goals of any successful
fire scene examination are to:
1. Determine the origin of the fire (where it began)
2. Determine the cause of the fire (the ignition source)
3. Locate, document, and preserve evidence that relates to the cause of the fire or associated criminal acts Whether the fire scene takes minutes, hours, or days to investigate, the basic procedures are the same. Fire scene investigations typically involve three broad areas: (1) witness interviews, (2) the physical examination, and (3)forensic or engineering analysis. Since each fire is different and the circumstances surrounding the fire are also different, the degree to which each component is involved varies from fire to fire.

## Slide 21
Depending on the complexity of the fire scene, one investigator can be responsible for the entire investigation or the duties can be delegated among numerous investigators. For example, one group of investigators may be solely responsible for the scene investigation, while another group conducts all the related interviews. When this occurs, coordination between the fire scene investigators and the witness interview teams is critical so that current information and data flows between the two groups.

## Slide 22
There are many other individuals who can provide useful information to fire investigators, including:
• Building owners and tenants
• Firefighters
• Contractors
• Insurance representatives
• Security services/alarm companies
• Local building officials
• Police officers

## Slide 23
The firefighters can provide valuable information relative to the location, behavior, and conditions of the fire, unusual odors, observations of unusual or suspicious activity, condition of the doors and windows, and the location and condition of victims. Contact with the first-responding firefighters is crucial in a fire investigation, particularly in cases where no eyewitness or other persons who observed the fire in its early stages can be found. investigators interview a firefighter about the fire and suppression activities to gain a better understanding of the fire spread.

## Slide 24
Information on repairs, renovations, or maintenance to the structure or its systems. Local building officials often can provide information related to building inspections and original or preexisting building permits and plans. Police officers

## Slide 25
Major issue that may be of concern during the analysis of fire scene debris relates to the presence of background contaminants or cross-contamination.
This information may be useful to the forensic chemist when conducting an analysis of the debris for the presence of ignitable liquids.
May be a presence of gasoline or a medium petroleum distillate naturally present at the scene well before the fire? Skilled investigators must obtain the answer to this question and others like it to assist forensic chemists in their evaluation of fire scene evidence.

## Slide 26: Exterior Fire Scene Examination
The ultimate goal of the fire scene examination is to identify the first fuels
ignited in the fire and the source of ignition. The ignition source must be
capable of causing ignition of the suspected initial fuel. For example, a single
paper match, while an ignition source, is not likely to ignite a solid oak log,
but that same match is easily capable of igniting a piece of newspaper. When

## Slide 27
The ignition source and the first fuel ignited are identified during the fire scene investigation, the cause of the fire may be established. Yet, the investigator must also explain how these two came together.
.

## Slide 28
Generally, all fires start from a single ignition source such as an open flame (match, candle) or a hot surface, and then grow in size to room fires and to large, structure fires. Thus, it is important to focus the fire scene investigation on the early stages of the fire in an attempt to identify the initial fuel and ignition source. To accomplish this task, the fire investigator must examine the fire scene in a systematic and deliberate manner, documenting the findings along the way

## Slide 29
The fire scene examination typically begins from the outside of the structure and later progresses inside. The investigator should remain objective and have no preconceived notion as to origin or cause. The obvious case may not be the cause, and one must delve into the fire scene to make a true judgment about what occurred. It is for this reason that the investigation must be conducted in a systematic and objective manner and must follow the scientific method.

## Slide 30
During the examination of the exterior, the location and description of
any heat or smoke damage to the structure should be noted. The examination
of the exterior and the telltale smoke and heat damage or patterns may give
a general indication about the origin of the fire, as shown in Figure 2.8. Items
removed from the scene by firefighters during overhaul may be found outside
and require a closer examination.
© 2004

## Slide 31
The condition of all doors, locks, or other points of entry should be evaluated, documented, and photographed. The utilities should be located and examined. The investigator must be aware of any items or materials that do not appear to belong in the area or seem to be out of place. For example, are any containers observed near the building?
Are there ladders present, allowing access to windows and roofs? Are tools or any other articles that do not appear to belong in the area lying near a window or door? The public areas around the scene should also be examined, including pathways, alleys, lawns, parking areas, or other places that could possibly contain items related to the scene. In the case of intentionally set fires, arsonists have been known to drop containers or other materials as they depart the area.

## Slide 32
A suitable perimeter around the fire scene should also be established at
this time, if not already established by fire department personnel. The perimeter
of the scene, typically established using crime-scene tape, will be used
to protect the integrity of the fire scene by limiting access to only those who
have official duties and whose entry is approved by the jurisdiction having
authority. The size of the perimeter should be large enough to include the
entire scene, any adjacent areas that are deemed relevant, and any remote
locations that may include evidence or other materials relevant to the investigation.

## Slide 33
In one case, an amateur arsonist unwittingly left his wallet outside the building while rolling on the ground to stop his clothes from burning. Responding firefighters found the wallet and gave it to fire investigators who made a quick arrest in the case. As you can see, examination of the exterior is a valuable piece of the overall fire scene investigation and should be conducted in a diligent manner to obtain all evidence related to the investigation.

## Slide 34
It may be necessary at times for the perimeter to be modified to include remote areas as the scene examination progresses. For example, if a gasoline container is found lying on a pathway a hundred feet from the structure, the perimeter should be expanded to include the pathway and the area up to the structure.

## Slide 35
It is also at this time that weather conditions should be noted, as weather can play a role in fire behavior.
Most important are the temperature, humidity, and wind conditions. Particular attention should be paid to the wind direction and speed as it can play a large role in fire spread, particularly in large fires.

## Slide 36: Interior Fire Scene Examination
At this time, the investigator should have the proper equipment to safely and successfully investigate the fire scene. The recommended minimum
equipment to be used during the fire scene examination includes:
Personal protective equipment
Flashlight (preferably lantern style) • Writing materials (clipboard or similar) • Assorted small tools or multipurpose tools (screwdrivers, wire cutters, knives)
Measuring devices (20- and 100-ft tape measures)
Camera, film, electronic media • Shovel or other hand tools • Rubber gloves • AC voltage tester

## Slide 37
Many factors can influence the size, intensity, and length of burn time
in a particular area. Nevertheless, it is an accepted practice to initially follow
the fire from the area of least damage to the area of greatest damage. During
this process, however, the investigator should continually assess contents,
interior finishes, ventilation, and other factors that may have influenced fire
behavior and resulted in greater-than-anticipated damage outside the area of
origin. As an example, firefighters arrive on the scene of a large-scale fire that
has been burning for 30 min and quickly suppress the fire in the area of
origin.

## Slide 38
Yet, other areas of the building may have become involved in the fire and subsequently burn for a considerable amount of time before suppressed.
This scenario will likely result in the area of origin having less damage than other areas of the structure that were involved at a later time and burned longer.
In this situation, witness statements and interviews with responding firefighters is critical in accurately identifying the area of origin. The fuel distribution and ventilation within a structure can also play a role in the growth of the fire.
A fire that originates in an area with minimal combustible materials and then spreads to areas that have a high concentration of readily combustible materials will likely result in a higher degree of fire damage outside the area of origin.