## Slide 1
Exercise No. 3
Measurement of Total, Shortwave and Longwave Radiation, and Its Estimation Using Planck’s Intensity Law

## Slide 2
In the absence of the Pyranometers, status of Global radiation reaching the surface of the earth could be computed by using it’s relationship with the bright sunshine hours. Global radiation (calories/cm2/day) is directly proportional to the ratio of actual and potential BSS hours.

## Slide 3: MEASUREMENT OF BRIGHT SUNSHINE
The bright sunshine is measured by means of the Campbell-Stokes Sunshine Recorder.
It was invented by John Francis Campbell in 1853 and modified in 1879 by Sir George Gabriel Stokes.
This consists of a glass sphere of 10 cm in diameter, mounted concentrically in a section of spherical bowl the diameter of which is such that the sun’s rays are focussed sharply on a card, held in the grooved cut into the bowl.
There is three overlapping pair of grooves each to take cards suitable in shape for different seasons of the year.
There should not be any obstruction having an elevation of 3o above the horizon.

## Slide 7
Campbell Stokes Bright Sunshine Recorder

## Slide 8
While inserting the new sunshine card, its 12-hr. line should be adjusted to coincide with the noon line engraved on the bowl.
The card is subdivided into hourly intervals.
As the sun moves across the sky, its focussed image burns a trace on the card, so that by measuring the trace for the whole day, the duration of sunshine during the day can be accurately recorded.
The total duration of sunshine can be obtained correct to 0.1 of an hour.
Thus sunshine is measured in number of hours per day.
For each day’s observation, sunshine cards should be inserted in the recorder before sunrise and removed after sunset.

## Slide 11
In the Northern hemisphere, the unit is set in a stand facing south to enable the maximum amount of sun to be recorded.
It is important to place the unit in an area where the sun will not be blocked by buildings, trees or flagpoles.
A modification to the standard unit for polar regions is the addition of a second, north facing, sphere and card, to record the sunlight during the summer when it remains in the sky for 24 hours.

## Slide 12: Procedures for recording sunshine measurements
Select the appropriate new card corresponding to the season concerned.
Insert the new sunshine card in the appropriate groove of the recorder and adjust it so that its 12-hr. line coincides with the noon mark engraved on the bowel.
Remove the burnt card in the evening after sunset and mark the date of observation on the reverse of the card.
Tabulate the amount of sunshine recorded during each hour of the day from sunrise to sunset using the special plastic scale.
Add up the values for all the hours and determine the total duration of sunshine hours of the day.

## Slide 13: Precautions for recording sunshine measurements
Do not clean the glass bowl of the sunshine recorder with any cloth or material that may abrade the surface. Avoid excessive vigour in polishing.
Remove immediately any deposit such as dew, frost, snow or bird droppings.
If the trace is not parallel to the central line of the card, or if the intensity of the trace is too high or too low, carry out levelling and other adjustments of the recorder.
Use the sunshine cards appropriate for the season.

## Slide 14
Computation of Global Radiation Intensity Using BSS
Angstrom in 1924 developed a regression equation to compute Total solar radiation (Rs) from BSS data.
This relates monthly average daily global radiation to the average daily sunshine hours, and is given by the following expression:
Rs = Ra [a+b (n/N)]
Where: Rs = Solar radiation at the surface.
Ra = Extraterrestrial Radiation at the top of the atmosphere, which differs with latitude;
a & b = Constants, a= 0.42 and b=0.30;
n = Actual bright sunshine (BSS) duration;
N= Maximum possible sunshine duration varies with latitude and time of season of a place

## Slide 15
Month | 00 | 100 | 200 | 300 | 400
January | 859 | 758 | 638 | 479 | 366
February | 887 | 821 | 729 | 620 | 497
March | 895 | 874 | 824 | 752 | 657
April | 869 | 896 | 897 | 870 | 815
May | 823 | 887 | 928 | 947 | 936
June | 793 | 875 | 935 | 974 | 987
July | 803 | 878 | 935 | 957 | 963
August | 842 | 885 | 930 | 898 | 867
September | 879 | 875 | 906 | 794 | 716
October | 885 | 835 | 848 | 663 | 548
November | 862 | 774 | 665 | 538 | 399
December | 846 | 737 | 611 | 465 | 329
Table. Mean Monthly values of Extraterrestrial Radiation (Cal/cm2/day) for different latitudes in Northen Hemishere

## Slide 16
Month | 00 | 100 | 200 | 300 | 400
January | 12.1 | 11.6 | 11.1 | 10.4 | 9.7
February | 12.1 | 11.8 | 11.5 | 11.1 | 10.6
March | 12.1 | 12.1 | 12.0 | 12.0 | 11.9
April | 12.1 | 12.3 | 12.6 | 12.9 | 13.2
May | 12.1 | 12.6 | 13.1 | 13.6 | 14.3
June | 12.1 | 12.7 | 13.3 | 14.0 | 15.0
July | 12.1 | 12.6 | 12.8 | 13.9 | 14.7
August | 12.1 | 12.5 | 13.2 | 13.2 | 13.8
September | 12.1 | 12.2 | 12.3 | 12.4 | 12.5
October | 12.1 | 11.9 | 11.7 | 11.5 | 11.2
November | 12.1 | 11.7 | 11.2 | 10.7 | 10.0
December | 12.1 | 11.6 | 10.9 | 10.3 | 9.4
Table. Maximum possible hours of Sunshine (N) for Different latitudes in Northen Hemisphere